RC-01 8w1

Programming and Operating Manual

Before programming the remote recommend that you read the entire manual.

It should keep this manual for further life.

INTRODUCTION

RC-01 8in1 is designed to support a variety of devices in the home. It is simple to program and easy to use. It is used to control the following devices:

- • TVs (CRT, LCD, Plasma, Projectors type)
• DVD, DVDs (DVD, DVD-R, DVD combo HDD and DVD Home Cinema System)
• VCR / COMBI VCRs (cassette recorder, video player, TV / VCR Combo and PVR)
• SAT / DVB
• Receivers TV (satellite receiver / set-top-box / DVB-S/DVB-T/SAT / HDD / converter / set-top-box/DVB-C)
• AUX
• Audio / Amplifier / Speaker System / Audio / Audio Receivers / Tuner / Amplifier / (DVD)
• Home Cinema

RC-01 8in1 combined with the above-mentioned devices using infrared signals. Before you use the remote control to operate these devices, it must be properly programmed.

BEFOR PROGRAMMING

Some special features and buttons on the remote work as follows:

LEARN

You can copy the function of a particular button on the original remote control for any button on the universal remote control.

MACRO

The sequence number assigned under one command button

CHECKING EQUIPMENT CODE

You can use this feature to check the code for each device.

Breakthrough VOLUME
You can activate or deactivate this function to control the volume and mute the TV operation mode other device, without having to switch devices.

Breakthrough OTHER FUNCTIONS
PLAY, REW, FF, REC, STOP, PAUSE, you can use directly for the control of VCR, DVD, VCD, CD, AMP, etc.., Under your TV, without having to switch devices.

Before using the remote control, you must program it according to the device to be controlled. Check out the information below to make sure that the remote control is properly programmed.

• Universal remote control works when it is directed toward the infrared receiver on the controlled device.
• Make sure that nothing is blocking the receiver to the controlled device.
• Do not leave exhausted batteries in the remote control, as it may cause leakage, which, as damage is not covered under warranty.
• Always replace both batteries at the same time, do not mix old and new batteries or mix batteries of different types at the same time.
• When throwing used batteries must be aware of the environment. Check with your local authority recycling center or to find out where the nearest point where you can leave your old batteries.
• Do not throw the remote control and the need to protect it from falls as they may cause damage to the device or the system.
• Make sure that the pilot is not exposed to liquid.
• Clean the remote control, use a dry cloth to ensure the long-term use.

INSTALLATION AND REPLACEMENT BATTERY

Install two new AAA batteries in accordance with the indications on the battery compartment. When the batteries are low and will need to be replaced, do so by following these steps:

A) Push up the catch on the lid of the battery compartment cover and slide it out of the main part of the back.
B) Carefully remove the old batteries and then place the new follow the signs "+" and "-".
C) When the batteries are already included, put a cover on the back, making sure the latch is in the right place.

PROGRAMMING YOUR REMOTE CONTROL AND ASSOCIATED EQUIPMENT

ENTERING THE CODE

The list of codes see what the codes are for the type and brand of device you want to control.
1 Turn on the device to be programmed to work with the remote control (TV, DVD, VCR, SAT, etc.).
2 Simultaneously press a button for a moment right choice of equipment and the switch of the [POWER] button until the LED lights.
3 Enter the four-digit code found previously in the code list.
4 If the code is correct, the LED will turn off and you can use the remote to control devices. If the code is not on the list, the LED flashes twice and will shine. It should then go back to the country and to make programming again.
5 After that, when the LED is off, check that the other keys such as [CH +] [CH-], [1], [2], [POWER] and so act accordingly. If the device does not respond to some or all of the commands sent by the remote control, go back to the second point, and enter a different four-digit code.

NOTE:

- We make every effort to ensure that the codes stored in the letter codes serviced by a large number of different models and brands of devices, but we can not guarantee that our universal remote control will operate each device. It may also happen that the pilot will operate some functions. For best results, enter the next code from the list or use the functions described below manual or automatic code search.

- If no button is pressed for 30 seconds, the device button flashes twice, turn off and light on the remote comes with the procedure code entry.

- When entering a four-digit code only use the numeric keypad. Pressing another button will exit the code entry procedure.

SPEED MANUAL PROGRAMMING CODES

If you still can not control the remote device after entering the code, or if you can not find the brand and code in the code list, use this function.
1 Turn on the device to be programmed to work with the remote control (TV, DVD, VCR, SAT, etc.).
2 Simultaneously press a button for a moment right choice of equipment and the switch of the [POWER] button until the LED lights.
3 Press [CH +] or [CH-] alone until the machine turns off. Each time when you press [CH + / -] button, the unit will light up. Once the device is turned on, you should refrain from pressing [CH + / -].
4 Press the OK button or any button on the device to save and exit.
5 Check that the various keys such as [CH +] [CH-], [1], [2], [POWER] and so act accordingly. If you are not satisfied with the result, go back to the second point and continue the search.

NOTE
1 In this mode, you can press the [CH +] to look forward and [CH-] to look back at the library of codes universal remote control.
2 Given the large number of remote control codes in the library, searching the database may take a long time for manual programming.

SPEED AUTOMATIC PROGRAMMING CODES

- If the two are not related methods result in the control device, try methods of automatic programming codes:
1 Turn on the device to be programmed to work with the remote control (TV, DVD, VCR, SAT, etc.).
2 Simultaneously press a button for a moment right choice of equipment and the switch of the [POWER] button until the LED lights.
3 Press the [POWER] switch on fast automatic programming codes. The pilot will broadcast the code [POWER] or [PLAY] or [0] at 1.5 seconds automatically. The LED lights up. When the device turns off immediately press [OK] to save and exit.

- NOTE
1 In this mode, you can press the [CH +] to look forward and [CH-] to look back at the library of codes universal remote control.
2 The device turns on and off when you use this function to search the entire library of codes.

DESCRIPTION OF OPERATION OPTIONS LEARN

This function copies the original signals from the remote control for a universal remote control RC-01 8in1. You can assign any function to any key.

LEARN - the introduction of a universal remote control functionality to

1 Press the device, such as [TV] button will light up. Press and hold for about 3 seconds the [LEARN]. The unit will light up.
2 Then point the infrared window of the original remote control toward the window universal remote RC-01 8in1 approximately 5 cm (set remotes facing each other, both toward the center).
3 Press the button on the original remote control whose function you want to remember. The device will flash during the entire process memory.
4 Press the button you want to store on the RC-01 8in1, the LED stops blinking and steady light, which means that the pilot is in the process of programming. If the LED flashes twice and exit the programming mode, it indicates a lack of sufficient memory.
5 Repeat steps 3 and 4 to program the required keys related to a specific device.
6 Then press the [LEARN] (or does not perform any operation for 20 seconds) to save the settings and exit the LEARN button, the device will turn off.
7 Repeat steps 1-6 to program the keys of other devices that you want to save on your remote control.

NOTE: The buttons on the remote control RC-01 8in1 for all devices, MACRO LEARN TV / AV, can not be reprogrammed.

DELETE MEMORY KEY

1 Press and hold the button whose function you want to erase. Then Press and hold the [POWER] at the same time until the LED on the key lights up, then release both buttons.
2 Please enter the OS [9990].
3 Then press the button you want to erase, the LED flashes twice slowly, erasing process is complete. If the LED flashes twice rapidly, this means that you can not erase the button.
4 In this case, repeat step three, to try again on a different key.

DELETE MEMORY OF ONE UNIT

1 Press and hold the device you want to erase function. Then Press and hold the [POWER] at the same time until the LED on the key lights up, then release both buttons.
2 Please enter the OS [9991].
3 When the pre-programmed keys are erased, the LED flashes twice and goes off.

MEMORY DELETE ALL DEVICES

1 Press and hold the device you want to erase function. Then Press and hold the [POWER] at the same time until the LED on the key lights up, then release both buttons.
2 Please enter the OS [9995].
3 When the pre-programmed keys of all devices will be erased, the LED flashes twice and goes off.

KEY PROGRAMMING MACRO

You can use this option to program the Macro keys to the one you press this button has been called the command sequence you selected.

As an example, we use the MACRO key functions: switching on TV, switch the TV to AV, the inclusion of DVD, "Play" in the DVD player.
1 Press and hold both the TV for a while and push button switch [POWER] button until the LED lights.
2 Please enter the OS [9960], the TV LED flashes twice and then lights up to indicate the entrance to the MACRO mode.
3 Press the [TV], [POWER], [AV], [DVD] [POWER], [PLAY] and then [OK] to save and exit MACRO programming.
4 If you press [MACRO], the pilot will automatically switch on the TV and switch the TV channel to AV, then turn to play the DVD player.

NOTE:
s You can program up to 15 buttons for this function. If you press more buttons to the device flashes twice, turn off automatically.

CHECKING THE CODE

You can use this option to see the four-digit code for each device. Do the following:
1 Press the device whose code you want to check, for example, [TV].
2 Press and hold the [POWER] and the number [1], [2], [3] or [4] at the same time and then release both buttons.
3 Notice how many times the LED flashes - the number of flashes indicates the code number.
NOTE:
1 If the code number is "0", the button will flash 10 times much faster.
For example: a four-digit code is "1095" then
[POWER] + [1]
The LED will blink 1 time
[POWER] + [2]
The LED will flash 10 times
[POWER] + [3]
The LED will flash 9 times
[POWER] + [4]
The LED will blink 5 times

Breakthrough VOLUME

Using this feature you can control buttons Volume + / - and Mute your TV (volume and mute) without switching the device on the TV. Follow the following steps to enable or disable this feature.
1 Press and hold the device and the [POWER] at the same time until the LED turns on, then release both buttons.
2 Enter the operation code [9100] to activate the function or operation code [9110] to deactivate. Following the action, the LED flashes twice.
3 Then, press the TV button, the LED flashes twice which shall terminate and exit.

Breakthrough OTHER FUNCTIONS

Using this feature, you do not move the TV mode to control the keys PLAY, REW, FF, REC, STOP, PAUSE other devices. Follow the following steps to enable or disable this feature.
1 Press and hold the TV and the [POWER] at the same time until the LED turns on, then release both buttons.
2 Enter the operation code [9120] to activate the function or operation code [9130] to deactivate. Following the action, the LED flashes twice.
3 Then, press the device you want to control, in addition to the TV, the LED flashes twice which shall terminate and exit.

DEFAULT SETUP

You can use this feature to restore the factory settings.
To put the remote control to the factory setting:
1 Press and hold any key with the [POWER] button until the LED turns on, then release the buttons.
2 Please enter the OS [9300], the LED blinks twice and turns off.
3 The pilot has been reset to factory settings.